ORIFICE
                                  =======
                                     
                      A Flowmeter Sizing Computation
     
                         by KYLE ENGINEERING, INC.
      
     ORIFICE is a  program meant to be used by  the practicing engineer
     as  an aid  to the  design of  orifices for  measurement of  fluid
     flow.  As such,  it is intended to supplement  rather than replace
     the  engineer's skill  and judgement.   Numbers generated  by this
     program   may  be  meaningless  or  even  incorrect  for  a  given
     application if input data have not  been wisely chosen.  It is the
     user's responsibility to employ this  program and its results in a
     sound and appropriate manner.
     
     This  program will  provide computer  aided sizing  techniques for
     the   most  common industrial  fluid  flowmeter,  the square  edge
     orifice  plate.  This  is  generally considered  the flowmeter  of
     choice in  2-inch and  larger pipe line  sizes for  clean liquids,
     gases, and  low velocity  vapor (including steam)  flows.  ORIFICE
     will calculate  new orifice  bores, recalculate range  changes for
     existing  orifice  systems,  and   determine  on-line  flows  from
     user-supplied process data.  
     
     The program  uses methods found  in two  books.  The first  is the
     classic text  "Principles and Practice of  Flow Meter Engineering"
     by  L. K.  Spink (copyright  by the  Foxboro Company),  edition 9.
     The other  is a  more recent  work, "Flow  Measurement Engineering
     Handbook", First  Edition, by  R. W.  Miller, which  describes the
     recently adopted  ISO/ASME orifice equations  and recommendations.
     The program user has the choice of either method.
     
     HOW IT WORKS
     
     Rigorous  calculation   of  orifice   performance  is   a  complex
     procedure.   The reader  is  advised  to refer  to  the two  books
     mentioned above for a  complete description of calculation method.
     Basic equations  for the calculation  as used in this  program are
     as  follows:
     
     ORIFICE - FUNDAMENTAL EQUATIONS 
     
     Specific to the spink universal equation:
      
          Wm = 359 S D^2 Fa Fm Fc Y1 (Gamma * hm) ^0.5
     
          where --
     
          S = (0.598 B^2) + (0.01 B^3) +
              (0.00001947 B^2 (10 B)^4.425)
     
              for flange taps
     












          S = (0.58925 B^2) + (0.2725 B^3) -
              (0.825 B^4) + (1.75 B^5)
     
              for pipe taps
     
          Fm = 1.0 for "dry" transmitters
     
          Fc = K/K1
     
          Kl = S/B^2
     
          K = Ko (1 + (Ef B/RD))  for flange taps
     
          K = Ko (1 + (Ep B/RD))  for pipe taps
     
          (See Buckingham equations # 119 - 129 in Spink, pages 527
            and 528 for additional information.)
     
          Gamma = Flowing Specific Weight (lbs./cu. ft.)
     
          Wm = Maximum Weight Flow Rate  (lbs./hr.)
     
          Wn = Normal Weight Flow Rate (lbs./hr.)
     
          RD = (6.32 Wn) / (Mu D) = Pipe Reynolds Number
     
     Specific to ISO/ASME equations  (Miller Sm method):
     
          qm = 358.9268 Sm Fa D^2  (Rho hw)^0.5
     
          where--
     
                  C Y1 B^2
          Sm = --------------
               (1 - B^4)^0.5 
     
          C = 0.5959 + (0.0312 B^2.1) - (0.184 B^8) + 
              (0.09 B^4 ) / (( D1 - B^4 )) - 
              (0.0337 B^3) / D + 
              (91.71 B^2.5) / RD^0.75
     
              for flange taps and D > 2.3 inches
     
     
          C = 0.5959 + (0.0312 B^2.1) - (0.184 B^8 + 
             (0.0399 B^4) / (1 - B^4) - (0.0337 B^3) / D +
             (91.71 B^2.5) / RD^0.75 
     
             for flange taps and 2< D < 2.3 inches
     
          C = ( (1-B^4)^0.5) (0.598 + 0.468 (B^4 + 10 B^12) +  
              (0.87 + 8.1 B^4) RD^-0.5)
     
            for flange taps and D< 2 inches
     












          C = 0.5959 + 0.461 B^2.1 + 0.48 B^8 +  
              (0.039 B^4) / (1 - B^4) +
              (91.71 B^2.5) / RD^0.75 
     
              for pipe taps
     
          Rho = Flowing Density (lbs./cu. ft.)
     
          qm = Maximum Mass flow rate (lbs./hr.)
     
          qn = Normal Flow Rate (lbs./hr.)
     
          RD = (6.32 qn) / (Mu D)
               (pipe reynolds number) 
     
     COMMON TO BOTH EQUATIONS
     
          hw = Operating Differential Pressure  (inches water column)
     
          D = Pipe Inner Diameter (inches)
     
          B = Orifice diameter / D  (Beta Ratio)
     
          Mu = Viscosity (centipoise)
     
          Fa = Thermal Correction Factor
               (Fitted Equations Based on charts in Spink, page 156,
               and Miller, page 9-17l.)
     
          k = Specific Heat Ratio
     
          Pf = Upstream Flowing Pressure (psig)
     
          pf = Pf + 14.7 (psia)
     
          X = hw / (27.7 pf)
     
          Y1 = 1 - (0.41 + 0.35 B^4) X/k
     
          for flange taps
     
          Y1 = 1 - (0.333 + 1.145 )B^2 +0.7 B^5 + 12 B^13) ) X/k
     
          for pipe taps
      
     INSTRUCTIONS ON DISK
     
     This  instruction  set  has  been  placed  on  the  disk  for  the
     convenience of  the user.  To  print out the instructions  on your
     printer   be  in   system  mode,   enter  the   instruction  "TYPE
     ORIFICE.DOC",  and    press  ENTER.   The  instructions   will  be
     displayed  on your  screen.   To get  a  hard copy  simultaneously
     press Ctrl and PrtSc prior to entering the TYPE command.
     
     PROBLEMS












     
     If you experience any difficulty  operating this software write or
     telephone Techdata at 
      
                               6615 la Mora
                             Houston, TX 77083
                              (713) 498-0797
      
     Even if  you do not  experience problems,  we'd like to  hear your
     comments about this  program -- what you like as  well as what you
     would like  to see changed.   Also please  let us know  what other
     types of engineering software would serve your needs.
     
     In case your disk  should  become damaged and unusable, return the
     disk with $10.00 and a replacement will be promptly sent.
     
     Techdata  supplies  other  engineering programs  and  also  offers
     custom  programming   for  chemical  and   mechanical  engineering
     applications on the PC.  Write or call for our catalog.
     
     * IBM Personal Computer is a trademark of IBM Corporation.
     Techdata is a trade name for Migliavacca, Inc.
     -----------------------------------------------------------------
     
     TECHDATA LICENSE AGREEMENT
     
     Important notice:   You should carefully read  the following terms
     and conditions  before running this program.   Running the program
     indicates your acceptance  of these terms and  conditions.  If you
     do not  agree with  them, you should  promptly return  the package
     and  your money will be refunded.
     
     
     1. ACCEPTANCE
     By use of the program  contained herein, Customer agrees to accept
     on  the  following terms  and  conditions  a non-transferable  and
     non-exclusive license to use said program.
     
     2.  TERM
     This Agreement shall be in  force from the date Customer purchases
     the  above  referenced  program   until  terminated  by  Customer.
     Customer may terminate the agreement  by returning to Techdata the
     original  program and  documentation  and any  and  all copies  of
     same.  Techdata  may terminate this Agreement  upon written notice
     to the Customer if Customer fails  to comply with any of the terms
     of this  Agreement.
     
     3.  LICENSE
     Each program  license granted under this  Agreement authorizes the
     Customer  to use  the program  on any  single computer  system.  A
     separate license is required for  each system on which the program
     is to be  used. This Agreement and any of  the licenses, programs,
     or  materials   to  which   it  applies   may  not   be  assigned,
     sublicensed, or  otherwise transferred  by Customer  without prior
     written consent  from Techdata.  No  right is granted to  print or












     copy the program in whole or part.
     
     4.  DISCLAIMER OF WARRANTY
     This program  is provided "as  is", without warranty of  any kind,
     either expressed  or implied, including,  but not limited  to, the
     implied   warranties  of   merchantability  and   fitness  for   a
     particular  purpose.   The  entire  risk as  to  the  quality  and
     performance of the program is  with you.  Should the program prove
     defective, you assume the entire  cost of all necessary servicing,
     repair, or correction.
     
     5.  LIMITATION OF LIABILITY
     In no  event will  Techdata be liable  for any  damages, including
     any lost  profits, lost  savings or  other direct,  incidental, or
     consequential damages arising  out of the use or  inability to use
     such program even if Techdata  has been advised of the possibility
     of such damages, or for any claim by any other party.
     
     6.  GENERAL
     If  any of  the provisions  of  this Agreement  are invalid  under
     statute or rule  of law in any  State, they are to  that extent to
     be  deemed omitted from this Agreement.
     
     11-7-84